## Slide 1: PRINCIPLES IN LAND USE MAPPING
Kapasa Makasa University
Bwalya Mutale

## Slide 2: What is land use mapping?
Land Use Mapping is the process of categorizing and visualizing how land is utilized by humans-such as agriculture, residential, commercial, industrial, transportation, recreational, etc.
Distinguishing from land cover

## Slide 3: Land Cover vs. Land Use:
Land Cover describes the physical material at the surface of the earth (e.g., vegetation, water, bare soil).
Land Use focuses on the function of land (e.g., cropland, urban development, industrial etc…).

## Slide 4: 1. Principle of Classification
Use of a standardized classification scheme (e.g., FAO, Anderson Classification System).
Categories must be mutually exclusive and collectively exhaustive.
Classes should reflect actual land use types: residential, industrial, recreational, agricultural, etc.

## Slide 5: 2 Principle of Scale
The map scale determines the level of detail.
Large-scale (e.g., 1:10,000) for local planning.
Small-scale (e.g., 1:250,000) for regional or national analysis.
Larger scales provide finer spatial resolution

## Slide 6: 3 Principle of Temporal Relevance
Land use data must be time-sensitive.
Changes in land use patterns over time are important for trend analysis.
Periodic updating is necessary to maintain map relevance.

## Slide 7: 4 Principle of Data Accuracy and Reliability
• Base data must be accurate, verifiable, and georeferenced.
• Use ground truthing, high-resolution imagery, and reliable datasets.
• Ensure positional accuracy and attribute accuracy

## Slide 8: 5 Principle of Consistency
Uniform methods and standards should be applied across different regions and time periods.
Ensures comparability and interoperability of maps.

## Slide 9: 6 Principle of Purpose and User Needs
Mapping should be goal-driven—whether for zoning, agriculture, urban planning, conservation, etc.
Stakeholder input is key in determining the functional classes to map.

## Slide 10: 7 Principle of Visual Representation
Use clear symbology, color codes, legends, and labels.
Maps should be interpretable by non-specialists.
Follow cartographic standards and ensure readability.

## Slide 11: LAND USE CLASSIFICATION SYSTEMS
Developed by the Food and Agriculture Organization (FAO) of the United Nations.
Designed to support global land resource assessment, agricultural statistics, and land use planning.
Main Land Use Categories:
Agricultural Land:
  Arable land, permanent crops, and pasture.
Forest Land:
  Areas under natural forest or forest plantations.
Urban and Built-up Land:
  Human settlements, infrastructure, industrial zones.

## Slide 12: Continue….
4. Wetlands: Permanent or seasonally flooded lands, marshes.
5. Other Land: Deserts, tundra, rock outcrops.
Key Features: Suitable for national reporting, policy development, and food security analysis. Aligns with international reporting obligations (e.g., SDGs, UNCCD).
Use Case: Governments use FAO classification for agricultural census and land productivity assessments.

## Slide 13: Anderson Land Use Classification System (USGS)
Developed in the 1970s by the U.S. Geological Survey (USGS).
Widely used in the United States for land use/land cover classification using remote sensing imagery, especially aerial photos.

## Slide 14: Continue…
Level I – General Categories:
Urban or Built-Up Land
Agricultural Land
Rangeland
Forest Land
Water
Wetland
Barren Land
Tundra
Perennial Snow or Ice

## Slide 15: Continue…
Level II – Specific Subclasses:
Urban: Single-family residential, multifamily residential, commercial, industrial, transportation
Agriculture: Row crops, pasture, orchards, vineyards
Forest: Deciduous, evergreen, mixed

## Slide 16
Key Features:
Designed to support classification using medium-resolution imagery (e.g., Landsat).
Level I suitable for broad national mapping; Level II adds detail for local or regional analysis.
Use Case: Useful for land cover change detection, urban sprawl studies, and resource planning in the U.S.

## Slide 17: CORINE Land Cover Classification (Europe)
CORINE = Coordination of Information on the Environment.
Initiated by the European Environment Agency (EEA) in 1985.
Aims to map land cover and land use across European countries using satellite imagery.

## Slide 18
Classification Structure:
Level 1: 5 broad classes (e.g., artificial surfaces, agricultural areas, forests and seminatural areas, wetlands, water bodies)
Level 2: Intermediate subclasses
Level 3: Very detailed categories (44 land cover classes)

## Slide 19: Examples of CORINE Classes
Artificial Surfaces: Continuous urban fabric, airports, industrial sites
Agricultural Areas: Arable land, permanent crops, pastures
Forest Areas: Broad-leaved, coniferous, mixed
Wetlands & Water Bodies: Inland marshes, coastal lagoons, rivers, lakes

## Slide 20
Key Features:Harmonized for cross-country comparison and EU-wide environmental policy support.
Updated every 6 years (e.g., 2000, 2006, 2012, 2018, 2022).
Data used for climate reporting, habitat monitoring, and urbanization tracking.
Use Case: European countries use CORINE for environmental monitoring, urban planning, and reporting to the EU.

## Slide 21
Thank you for your attention
“Discipline is true freedom”