## Slide 1
TOOLS FOR LAND USE MAPPING
Lecturer: Mr.B.Mutale
Kapasa Makasa University

## Slide 2
INTRODUCTION
Setting the stage: Why do we need specialized tools for mapping the Earth's surface?

## Slide 3
Food Security
Monitoring agricultural land use to predict crop yields and manage irrigation in Zambia’s Muchinga province.
Urban Planning
Tracking rapid urban expansion in Chinsali and Lusaka to provide sustainable infrastructure and services.
WHY MAPPING MATTERS

## Slide 4
Understanding the Difference
Land Cover: The physical material at the surface (e.g., forest, water, soil).
Land Use: The human activity or economic function of that land (e.g., recreation, grazing, residential).
LAND USE VS. LAND COVER

## Slide 5
Planning
Defining scope & tools
Acquisition
Sensing & GPS
Processing
GIS Analysis
Validation
Field verification
Dissemination
Maps & Reports
THE MAPPING WORKFLOW

## Slide 6
Remote Sensing
Satellites, Aircraft, Drones
Field Survey
GPS/GNSS, Mobile Apps
Software/GIS
Analysis & Storage
MAIN TOOL CATEGORIES

## Slide 7
REMOTE SENSING
Eyes in the sky: Data from a distance.

## Slide 8
The Gold Standard
•
50+ years of continuous Earth records.
•
Resolution: 30 meters (Perfect for regional mapping).
•
Availability: Completely Free.
•
Essential for tracking deforestation trends in Zambia since the 1970s.
NASA/USGS LANDSAT

## Slide 9
High-Frequency Monitoring
Provides 10-meter resolution images every 5 days globally.
13 spectral bands allow for sophisticated vegetation analysis (NDVI) and agricultural health monitoring.
ESA SENTINEL-2

## Slide 10
PlanetScope: Daily imagery of the whole world at 3m resolution.
WorldView: Sub-meter resolution (30-50cm) for identifying individual buildings or trees.
Maxar/DigitalGlobe: Industry leaders in commercial high-res tasks.
Application: Critical for urban cadastral mapping and security monitoring.
VERY HIGH RESOLUTION (VHR)

## Slide 11
Cloud Penetration
Synthetic Aperture Radar (SAR) like Sentinel-1 uses microwave pulses that pass through clouds, smoke, and rain.
Day/Night Capability
Active sensors provide their own light source, allowing mapping during the night—crucial for flood monitoring during Zambia's rainy season.
RADAR MAPPING (SAR)

## Slide 12
Precision on Demand
Drones (UAVs) provide centimeter-level resolution (GSD) for small project areas.
Use Case: Creating high-fidelity maps for Chinsali municipal planning or individual farm plot monitoring.
UNMANNED AERIAL VEHICLES

## Slide 13
3D Structure Mapping
Uses laser pulses to measure distance.
Can "see through" tree canopies to map the terrain (Digital Terrain Model) and measure forest biomass with incredible accuracy.
LIDAR TECHNOLOGY

## Slide 14
FIELD SURVEY & GNSS
Ground-truthing and absolute positioning.

## Slide 15
Beyond "GPS"
Global Navigation Satellite Systems (GNSS) include:
Positional Accuracy
The accuracy depends on the number of satellites in view and the receiver quality. Essential for fixing land boundaries.
•
GPS (USA)
•
GLONASS (Russia)
•
Galileo (Europe)
•
BeiDou (China)
GNSS BASICS

## Slide 16
Differential & RTK
Real-Time Kinematic (RTK) GPS provides 1-3cm accuracy by using a base station and a rover.
Professional brands like Trimble, Leica, and Topcon are common in Zambian civil engineering and survey firms.
SURVEY-GRADE HARDWARE

## Slide 17
KoboToolbox
Free, open-source tool for field data collection on Android devices. Used for social surveys and ground-truthing.
ArcGIS Field Maps
Mobile app for field workers to view and update GIS maps in real-time synced with the office.
Avenza Maps
Allows use of geo-referenced PDF maps offline. Great for forest patrol and remote areas.
MOBILE DATA COLLECTION

## Slide 18
GIS & ANALYSIS TOOLS
Turning raw data into intelligence.

## Slide 19
Industry Standard
Powerful spatial analysis tools.
Extensive documentation and support.
Cloud integration (ArcGIS Online).
DESKTOP GIS: ARCGIS PRO

## Slide 20
Open Source Champion
Completely free and open-source. Used extensively in KMU student projects.
Supports almost every spatial data format and offers thousands of user-developed plugins.
DESKTOP GIS: QGIS

## Slide 21
Big Data Processing
A cloud-based platform for multi-petabyte geospatial analysis.
Students can use JavaScript or Python to analyze 40 years of satellite data for the whole of Zambia in seconds.
CLOUD GIS: GOOGLE EARTH ENGINE

## Slide 22
AI & AUTOMATION
Machine Learning in Land Use Classification.

## Slide 23
Automating Maps
Instead of manual tracing, we use algorithms to recognize land use types.
Supervised Learning: You teach the computer by providing "training samples" of known land types.
IMAGE CLASSIFICATION TOOLS

## Slide 24
Segments, Not Pixels
OBIA groups pixels into meaningful objects based on shape, texture, and relationship to neighbors.
High-Res Necessity
Critical for analyzing drone and VHR satellite imagery where pixel-based methods often fail (the "salt and pepper" effect).
OBJECT-BASED ANALYSIS (OBIA)

## Slide 25
ESA WorldCover
Global 10m land cover product based on Sentinel-1 and 2 data.
Global Forest Watch
Real-time alerts and data on forest loss and gain.
NASA Earthdata
One-stop shop for all NASA satellite datasets.
ONLINE DATA REPOSITORIES

## Slide 26
Crowdsourced Mapping
The "Wikipedia of Maps." Volunteers globally map roads, buildings, and land use.
Importance: Most mapping in Chinsali is updated by OSM contributors, providing a vital base layer for planners.
OPENSTREETMAP (OSM)

## Slide 27
Local Institutional Tools
•
ZMA: Zambia Ministry of Agriculture portals.
•
Zambia Statistics Agency: Demographic spatial data.
•
Deforestation tracking: Tools used by the Forestry Department and MLNR.
THE ZAMBIAN CONTEXT

## Slide 28
Hyperspectral Imaging: Hundreds of bands for detecting soil minerals or specific plant diseases.
Real-time Streaming: Satellite video and live-updating maps.
Edge Computing: Drones processing classification data onboard in real-time.
Participatory GIS: Local communities using apps to map their own indigenous land use.
FUTURE TRENDS IN MAPPING

## Slide 29
Mapping Bias
Who is being mapped? Who is doing the mapping? We must ensure mapping reflects local reality, not just external priorities.
Data Privacy
With high-res imagery, individuals' privacy can be compromised. Regulations are evolving to manage these risks.
ETHICS & CONSIDERATIONS

## Slide 30
QUESTIONS & DISCUSSION
Thank you for your attention.